## Slide 1: Electricity

## Slide 2
Electric Charge Rules:
  More protons than electrons: + charge
  More electrons than protons: - charge
    So if an atom gains an electron, it becomes a negatively charged ion
  Like charges repel; opposite charges attract
    Causes the flow
  In electricity, ONLY e- move, not protons!
Strength of electric force due to
  Quantity of charge involved
  How far apart the charges are
Electric Charge

## Slide 3
Electric Field: region around charged particles in which others will attract or repel
  Note: Strength of the field depends on
    amount of charge produced
    distance from charge
Electric Field

## Slide 4: Static Electricity and Charging
Charge can be transferred by friction, contact, and by induction
Friction
  Ex
    rubbing a balloon against your hair
    walking across a carpet
Contact
  Ex - Touching a Van de Graff generator
Induction - when charge is transferred without contact
  A neutral metal comb becomes charged by being held near a charged object

## Slide 5
Electric Current: flow of e- through a wire
  Symbol for current is I
  Current is measured in amperes, or amps (A) for short
     current =  e-
Flow of Electricity

## Slide 6
Resistance: opposition to flow of electricity
  Symbol for resistance is R
  Resistance is measure in ohms, which is represented by Ω
  Poor conductors have high resistance (or low conductivity)
    Ex. Iron
  Good conductors have low resistance (or high conductivity)
    Ex. Copper
  Long and thin wires have more resistance than short and thick wires
    Resistance is affected by a material’s thickness, length and temperature
  Any device that you plug in is called a resistor (load)
Notes: Increase in temp leads to increase in resistance
Increase length leads to increase in resistance
Decrease in thickness leads to increase in resistance

## Slide 7
Conductors & Insulators
  Conductor – material charge can flow through easily
    Ex – metal such as copper and silver
  Insulator – material charge can not flow through easily
    Due to electrons being tightly bound to its atoms
    Ex. – wood, plastic, rubber, air, glass
Flow of Electricity

## Slide 8
Ohm’s Law:
  current in a wire =voltage/resistance (I=V/R)
Current Directions:
  Direct Current (DC): electrons flow in the same direction
    Ex. Batteries (e- flow through and terminal)
  Alternating Current (AC): Electrons constantly change their direction of flow
    Ex. Electricity from power plants (via generators); therefore the electricity in your home and school is mostly alternating current.
    The electricity from power lines needs to go through a step-down transformer before it can be used by your home
Power (P) = voltage (V) X current (I)
  (watts = volts X amps)
Flow of Electricity cont.,

## Slide 9
https://www.youtube.com/watch?v=FIlFcoPAwdM
Flow of Electricity cont.,

## Slide 10
What’s a Circuit?
  Provides a complete, closed path for an electric current to flow
  Circuit works when path is closed; doesn’t work when path is open
Parts of a Circuit:
  A source of e- (i.e. battery, outlet)
  A load (resistance) which is the device that uses the electricity
  Wires carry the electrons
  A switch, which opens or closes the circuit
Electric Currents

## Slide 11
Only one path for a current to flow
All parts of the circuit are connected one after the other
  Ex. Old Christmas Lights
Same current (I) passes through each resistor
Current stays the same
Voltage drops after each resistor
Series Circuit

## Slide 12
Different parts of circuit are on separate branches
Several paths for electrons can be taken
  Ex. New Christmas Lights
  Ex. Circuits in your home
Voltage stays the same
Current decreases through each branch
Parallel Circuit

## Slide 13: Electrical Safety
Fuse
  Wire in the center of the fuse melts when too much current passes through it
Circuit Breaker
  A switch opens when the current is too high
Ground-fault circuit interrupter (GFCI)
  Monitors current flowing to and from an outlet or appliance
  If current is not equal →current is escaping and the GFCI opens the circuit to prevent serious electric shock

## Slide 14: Magnetism

## Slide 15: Magnetism
All magnets have North and South poles
  If you break a bar magnet in half, each half will become a bar magnet with two poles
Rule for magnetic poles: like poles repel/opposites attract
Magnetic Field = region in which magnetic forces can act
  Earth has one around it (Magnetosphere); strongest at poles
  Magnetic lines of force define these areas
  Electrons in atoms spin, causing the magnetic field
Magnetic Force – as two magnets move farther apart, the magnetic force ↓

## Slide 16
Electricity and magnetism are inseparable
Electromagnet: made by winding wire around an iron core
  Will have N and S poles
  Polarity of magnet depends on polarity of electric current
Magnetism can induce electricity
Electricity can induce magnetism
Electromagnetism

## Slide 17
Electric Wire wrapped around an iron core
These are temporary magnets; can be turned on and off
  Ex. Doorbells, telephones, electric motors
Moving a magnet inside a coil of wire will induce a voltage in the coil
  The faster the magnet moves → the higher the voltage
Electromagnets

## Slide 18
Changes mechanical energy into electrical energy
Loop of wire (conductor) spins inside a magnetic field to create electricity; known as an electromagnetic induction
Most of the power you use everyday comes from generators
  Burning of fossil fuels creates steam that spins a turbine which will turn the coils in a generator
  In Michigan, the major source of fossil fuel is coal
Electric Generator